## Slide 1: Plant Utility System (TKK-2210)
14/15 Semester 4
Instructor: Rama Oktavian
Email: rama.oktavian86@gmail.com
Office Hr.: M-F 13-15

## Slide 2: Boilers

## Slide 3: Boilers
Apa itu boiler?
Kenapa membutuhkan boiler?
Rangkaian peralatan untuk mengubah energi kimia dalam bahan bakar menjadi energi termal atau panas laten dalam uap.

## Slide 4: Boilers
4
BURNER
WATER SOURCE
BRINE
SOFTENERS
CHEMICAL FEED
FUEL
BLOW DOWN SEPARATOR
VENT
VENT
EXHAUST GAS
STEAM TO PROCESS
STACK
DEAERATOR
PUMPS
Figure: Schematic overview of a boiler room
BOILER
ECO-NOMI-ZER

## Slide 5: Boilers
Sub – sub peralatan pada boiler

## Slide 6: Boilers
Sub – sub peralatan pada boiler

## Slide 7: Boilers
Industrial boilers
    Steam generators
    Closed vessels
    made of steel and
    used for generation of steam
    vaporizing water
    combustion of fuels
    eg. coal,coke,oil,wood,saw dust and begesse etc.
    Steam used for producing power,for industrial process work or for heating proposes.

## Slide 8: Boilers
A closed vessel in which steam is produced from water by combustion of fuel
STEAM BOILERS

## Slide 9: Boilers
Purpose of boilers
For generating power in steam engines or steam turbines
In textile industries for sizing and bleaching
For heating the buildings in cold weather and for producing hot water for hot water supply

## Slide 10: Boilers
Primary requirements of a boiler
The water must be contained safely
The steam must be safely delivered in desired condition (as regard its pressure, temperature, quality and required rate)

## Slide 11: Boilers
Steam boiler accessories
Feed pumps: Used to deliver feed water to the boiler. It is desirable that the quantity of water supplied should be at least equal to that evaporated and supplied to the engine
Injector: to feed water into the boiler
Economizer: a device in which the waste heat of the flue gases is utilized for heating the feed water
Air pre-heater: to increase the temperature of air before it enters the furnace.

## Slide 12: Boilers
Steam boiler accessories
Economizer

## Slide 13: Boilers
Steam boiler accessories
Air pre-heater

## Slide 14: Boilers
Steam boiler accessories
Super heater: to increase the temperature of the steam above its saturation point
Steam consumption of the engine or turbine is reduced
Efficiency of the steam plant is increased
Losses due to condensation in the cylinders and the steam pipes are reduced.
Why we use superheated steam?

## Slide 15: Boilers
Steam boiler accessories
Super heater: to increase the temperature of the steam above its saturation point

## Slide 16: Boilers
Classification of boilers
Horizontal, vertical or inclined
Fire tube and water tube
Externally fired and internally fired
Forced circulation and natural circulation
High pressure and low pressure
Stationary and portable
Single tube and multi tube

## Slide 17: Boilers
Fire tube boilers
If hot gases are inside the tube and water is outside the tube

## Slide 18: Boilers
Water tube boilers
If water is inside the tube and hot gases are outside the tube

## Slide 19: Boilers
Water tube boilers

## Slide 20: Boilers
Water tube boilers

## Slide 21: Boilers
Water tube boilers

## Slide 22: Boilers
Comparison of water tube and fire tube boiler
Particulars | Fire-tube boilers | Water-tube boilers
Position of water and hot gases | Hot gases inside the tubes and water outside the tubes | Water inside the tubes and hot gases outside the tubes
Mode of firing | Generally internally fired | Externally fired
Operation pressure | Limited to 16 bar | Can go up to 100 bar
Rate of steam production | Lower | Higher
Suitability | Not suitable for large power plants | Suitable for large power plants
Risk on bursting | Involves lesser risk of explosion due to lower pressure | More risk on bursting due to high pressure
Floor area | For a given power it occupies more floor area | For a given power it occupies less floor area
Construction | Difficult | Simple

## Slide 23: Boilers
Comparison of water tube and fire tube boiler
Particulars | Fire-tube boilers | Water-tube boilers
Transportation | Difficult | Simple
Shell diameter | Large for same power | Small for same power
Chances of explosion | Less | More
Treatment of water | Not so necessary | More necessary
Accessibility of various parts | Various parts not so easily accessible for cleaning, repair and inspection | More accessible
Requirement of skill | Require less skill for efficient and economic working | Require more skill and careful attention

## Slide 24: Boilers
Classification of boilers based on combustion equipment
Solid fuels fired
Hand fired
Stoker fired
Pulverized fuel fired
Underfeed stockers
Overfeed stockers
Unit system
Central system
Both

## Slide 25: Boilers
Travelling grate stoker

## Slide 26: Boilers
Spread stoker

## Slide 27: Boilers
Pulverized fuel firing

## Slide 28: Boilers
Classification of boilers based on combustion equipment
Liquid fuel fired
Injection system
Evaporator system
Combination of both

## Slide 29: Boilers
Classification of boilers based on combustion equipment
Gaseous fuel fired
Atmospheric pressure system
High pressure system

## Slide 30: Boilers
Boiler control
Basic control:
- Feed water and drum level control
- Steam pressure control
- Steam temperature control

## Slide 31: Boilers
Boiler Mountings and Accessories
Fitting and devices which are necessary for the safety and control are knows as boiler mountings
Fitting or devices which are provided to increase the efficiency of the boiler and help in the smooth working of the plant are knows as boiler accessories.
Fittings which are essential from the safety point of view are as follows,
Water level indicators
Safety valves
Combined high steam and low water safety valve
Fusible plug

## Slide 32: Pressure gauge
To record the steam pressure at which steam is generated in the boiler
A bourdon pressure gauge in its simplest form consists of a simple elastic tube
One end of the tube is fixed and connected to the steam space in the boiler
Other end is connected to a sector through a link

## Slide 33: Pressure gauge

## Slide 34: Fusible plug
To extinguish fire in the event of water level in the boiler shell falling below a certain specified limit
It is installed below boiler’s water level

## Slide 36: Steam stop valve
A valve is a device that regulates the flow of a fluid (gases , fluidized solids slurries or liquids) by opening or closing or partially obstructing various passageways
Function : to shut off or regulate the flow of steam from the boiler to the steam pipe or steam from the steam pipe to the engine

## Slide 37: Steam stop valve

## Slide 38: Feed check valve
To allow the feed water to pass in to the boiler
To prevent the back flow of water from the boiler in the event of the failure of the feed pump

## Slide 39: Blow off cock
To drain out water from the boiler for internal cleaning inspection or other purposes

## Slide 40: Efisiensi boiler
Evaluasi kinerja boiler
Neraca energi pada boiler

## Slide 41: Efisiensi boiler
Energy losses

## Slide 42: Efisiensi boiler
Efisiensi termis boiler
“ persen energi (panas) masuk yang digunakan secara efektif pada steam yang dihasilkan.”
Ada dua metode yang digunakan:
Metode langsung: energi yang didapat dari fluida kerja (air dan steam) dibandingkan dengan energi yang terkandung dalam bahan bakar boiler.
Metode tak langsung: efisiensi merupakan perbedaan antara kehilangan dan energi yang masuk.

## Slide 43: Efisiensi boiler
Metode langsung

## Slide 44: Efisiensi boiler
Metode langsung

## Slide 45: Efisiensi boiler
Metode tak langsung
British Standard, BS 845:1987 dan USA Standard ASME PTC-4-1 Power Test Code Steam Generating Units .

## Slide 46: Efisiensi boiler
Metode tak langsung
British Standard, BS 845:1987 dan USA Standard ASME PTC-4-1 Power Test Code Steam Generating Units .

## Slide 47: Efisiensi boiler
Metode tak langsung

## Slide 48: Efisiensi boiler
Metode tak langsung

## Slide 49: Efisiensi boiler
Metode tak langsung

## Slide 50: Efisiensi boiler
Metode tak langsung

## Slide 51: Efisiensi boiler
Metode tak langsung

## Slide 52: Efisiensi boiler
Metode tak langsung

## Slide 53: Efisiensi boiler
Metode tak langsung

## Slide 54: Efisiensi boiler
Metode tak langsung

## Slide 55: Efisiensi boiler
Metode tak langsung

## Slide 56: Efisiensi boiler
Metode tak langsung

## Slide 57: Efisiensi boiler
Metode tak langsung

## Slide 58: Efisiensi boiler
Metode tak langsung

## Slide 59: Efisiensi boiler
Metode tak langsung

## Slide 60: Efisiensi boiler
Metode tak langsung

## Slide 61: Efisiensi boiler
Metode tak langsung

## Slide 62: Efisiensi boiler
Case study
Sebuah boiler menggunakan bahan bakar minyak kualitas tinggi (hanya berisi hidrokarbon) yang memiliki panas pembakaran standar – 43.515 J g-1 pada 25 C dengan CO2(g) dan H2O(l) sebagai produk. Temperatur bahan bakar dan minyak masuk ke ruang pembakaran pada 25 C. Udara dianggap kering. Gas hasil pembakaran keluar dari boiler pada 300 C, dan analisis rata-ratanya adalah (basis kering) 11,2% CO2, 0,4% CO, 6,2% O2 dan 82,2% N2. Berapa bagian dari panas pembakaran yang ditransfer sebagai panas ke boiler?

## Slide 63: Efisiensi boiler
Solution
Basis: 100 mol gas hasil pembakaran kering:
CO2 11,2 mol
CO 0,4 mol
O2 6,2 mol
N2 82,2 mol
------------------------
Total 100,0 mol
NERACA O2
Masuk
O2 masuk (dalam udara) = 21,85 mol
Keluar
Dalam CO2 = 11,20 mol
Dalam CO = 0,20 mol
O2 sisa = 6,20 mol
---------------------------------------------
Total O2 selain H2O = 17,60 mol
Jadi O2 yang bereaksi membentuk H2O = 21,85 – 17,6 = 4,25 mol
H2O yang terbentuk = 2 (4,25) = 8,50 mol
Total O2 yang bereaksi = 11,2 + 0,2 + 4,25 = 15,65 mol
Neraca massa C
keluar
Sebagai CO2 = 11,20 mol
Sebagai CO = 0,40 mol
---------------------------------------
Total = 11,60 mol
Masuk
Mol C masuk = mol C keluar = 11,60 mol
NERACA H2
Keluar
Sebagai H2O = 8,50 mol
Masuk
Mol H2 masuk = mol H2 keluar = 8,50 mol
C dan H2 semuanya berasal dari bahan bakar, sehingga total berat bahan bakar yang masuk adalah = (11,60) (12) + (8,50) (2) = 156,2

## Slide 64: Efisiensi boiler
Solution
Jika semua bahan bakar terbakar sempurna membentuk CO2(g) dan H2O(l) pada 25C, maka panas pembakarannya adalah:
Analisis hasil pembakaran menunjukkan bahwa pembakaran berlangsung tidak sempurna dan H2O berupa gas bukan cairan.
Reaksi yang terjadi
C11,6H17(l) + 15,65 O2(g)  11,2 CO2(g) + 0,4 CO(g) + 8,5 H2O(g)
Reaksi di atas merupakan penjumlahan dari reaksi2 sbb.:
C11,6H17(l) + 15,85 O2(g)  11,6 CO2(g) + 8,5 H2O(l)
8,5 H2O(l)  8,5 H2O(g)
0,4 CO2(g)  0,4 CO(g) + 0,2 O2(g)
Panas reaksi standar total pada 25C:
Reaktan pada 1 bar
dan 25C:
fuel 152,2 g
O2 21,85 mol
N2 82,20 mol
Produk pada 1 bar
dan 300C:
CO2 11,2 mol
CO 0,4 mol
H2O 8,5 mol
O2 6,2 mol
N2 82,2 mol
Jika dimasukkan ke persamaan untuk HP:
= 940.660 J
= – 6.309.740 + 940.660 = – 5.369.080 J
Proses pembakaran ini merupakan proses alir tunak dengan:
WS = 0
EK = 0
EP = 0
Maka: H = Q
Q = – 5.369.080 J merupakan panas yang ditransfer ke boiler
Jadi fraksi panas pembakaran yang ditransfer ke boiler adalah:

## Slide 65
Thank You !